# Glider toolbox
## Introduction
The proposal is to develop a MATLAB toolbox (compatibility with Octave is desirable) for glider data processing based on the existing work by Tomeu Garau. The initial version is for Slocum gliders only. The toolbox should allow the following features as independent operations:
1. Process glider data in real time. Either from
  1. Native Slocum data format: binary data (sbd, mbd, dbd and tbd, nbd, ebd), surface logs and operational parameters.
  2. ASCII Converted Slocum data format: ascii data and helper loaders.
  3. NetCDF version of the above data.
2. Process glider data in delayed time.
## Data structures and conversion
The data collected by the glider comes in binary files that may be converted to ascii dat files with companion m-files to load the data from Octave/MATLAB. The description of the binary files and the conversion process is explained here:
http://rucool.marine.rutgers.edu/manuals/glider/slocum-glider-data-files-primer/
The contents of that binary files are described here:
http://marine.rutgers.edu/~kerfoot/slocum/masterdata/source/masterdata_07_09.html
The binary files are organized per missions and segments. Each glider deployment may be composed of several missions (new missions are triggered by the pilot). Each mission is built of segments (a new segment is started each time the glider goes to surface). There is a file for each segment named after the mission and the segment.
The conversion above mentioned is oriented to produce tabular data which is loaded as a matrix. Since the glider configuration may be updated, the segment files may have different number of variables, that is different number of data columns.
Internally, the segments are composed of a series of yos, each one build of a downcast/dive and an upcast/climb. Internally the missions may be divided in transects. A transect is a sequence of segments moving from one commanded waypoint to the next one.
For the processing of the data of the whole deployment, the following structure is proposed:
1. Struct with metadata and data fields
  1. data field is a struct with a time serie field for each sensor or variable. It is convertible to a tabular view of the data with struct2array. The reverse conversion is possible with the composition of num2cell and cell2struct.
  2. metadata field is a struct whith fields describing the above dataset.
    1. The sources field contains a list of the original files the data comes from.
    2. The sensors field contains a list of the variables in the glider data set. It should match the field name list of the above data structure. Index of a sensor in this list should match the column number of the sensor in a tabular view of the data.
    3. The units field contains a list of the units of measurement for each sensor. For raw data this are the units reported by the device (even if they are wrong or missing).
## Processing parameters and metadata
The following parameters of the glider or the deployment are currently used:
1. Glider name.
  It was in deployment info in json file.
  It is platform name from data base.
  Used across processing chain:
  1. When creating base path for glider deployment/mission data directory tree as constant expression from variable initialized with deployment struct member.
  2. In function downloading dockserver files (should match internal glider name) as input argument from variable initialized with deployment struct member.
  3. In function generating NetCDF files when initializing file name as constant expression from input argument initialized from member of deployment struct (also passed as input argument)
2. Deployment/mission name.
  It was in deployment info in json file.
  ?? It is deployment name from data base.
  Used:
  1. When creating base path for glider deployment/mission data directory tree as constant expression from deployment struct member.
  2. When creating base path for glider deployment/mission images as constant expression from deployment struct member.
3. Dockserver parameters: url (ip), user and password.
  It was in glider configuration file.
  Used in function downloading files from dockserver from deployment structure passed as input argument.
4. Deployment data root (a.k.a. ${BASE_PATH}).
  It was hard coded in main script as default value (or config file or json file but it does no seem to be there) and assigned to deployment struct member.
  Used:
  1. When creating base glider deployment/mission directory tree.
  2. In function downloading files from dockserver from deployment structure passed as
  3. In function generating NetCDF files from deployment structure passed as input argument.
5. Names for glider subdirectory tree:
   ${BASE_PATH}/${GLIDER}/${DEPLOYMENT}/{binary,ascii,log,mat,netcdf}
  It was in configuration section in main script and also hard coded in function downloading files from dockserver.
  Used:
  1. In function downloading files from dockserver (target directories for binary and log files) from hard coded directory names and deployment struct member dataRoot.
  2. Input arguments of function converting binary files to ascii.
  3. In function generating NetCDF files when initializing local file name as constant expression from hard coded string literal.
6. Deployment start and end date:
  It was in deployment info in json file.
  It is initial date and end date from data base.
  Used:
  1. In function downloading files from dockserver from deployment structure passed as input argument.
  2. In function converting binary files to m-loaders when initializing the period input argument used to convert only the files that belong to the deployment.
  3. In function loading glider data from m-loaders when initializing the period input argument used to load only the files that belong to the deployment.
  4. In function generating NetCDF files when initializing file name as constant expression from deployment structure passed as input argument
7. Directory for configuration files.
  It was in configuration section in main script.
  Used:
  1. As base path for glider configuration files
  2. As base path for sensor filter file passed to binary data conversion function.
8. Sensor filter configuration file full name.
  It was hard coded in binary conversion function call (builded from configuration directory option and hard coded file name).
9. Deployment initial location
  It is inferred from data.
  Used:
  1. As global atribute for NetCDF files in genRawGliderNcFile.
10. Processing options: scientific time filling, pressure filtering.
  Set in processing options struct in configuration section of main script.
  Used:
  1. In function processing glider data from struct passed as input argument.
11. Default pitch value when pitch sensor is missing.
  Hardcoded in processGliderData.
12. Desynchronized data time threshold.
  Hardcoded in processGliderData.
13. Profile maximum relative depth gap and profile minimum depth range.
  Hardcoded in findProfiles.
14. Processing options: temperature and conductivity sensor lag correction.
  Encoded in string field of processing options struct in configuration section of main script as 'T' and 'C'.
  Used:
  1. In function processing glider data after parsing string field in options struct passed as input argument.
15. Processing options: salinity thermal lag correction.
  Encoded in string field of processing options struct in configuration section of main script as 'TH'.
  Used:
  1. In function processing glider data after parsing string field in options struct passed as input argument.
16. Default minimization options.
  Coded in static function buildMinizationOptions.
  Used:
  1. In function estimating sensor lag parameter when initializing local variable.
  2. In function estimating thermal lag parameter when initializing local variable.
17. Variables to be gridded.
  Hard coded in glider data gridding function.
  Used:
  1. In glider data gridding function.
## Comments on relevant functions
GetDeploymentsRemotely:
Get active deployment list from Gapp URL and parse the JSON output to a structure containing deployment parameters and tracking data from the surface logs.
ConvertSlocumBinaries:
Convert binary data to m-files and dat-files using executables provided by manufacturer.
To perform the conversion, the binary files are copied to a temporary file which is removed later.
If there are both scientific and navigation files, the conversion is performed based on the scientific ones, trying to merge them with the appropiate navigation file.
  - How to associate a navigation file for each segment scientific file?
    - Currently the most extensive is choosen.
  - What happens when there are several scientific files but only one navigation file for a segment?
    - This is the worst case. Since the binary that converts from ascii data to m-loaders sets the names of the files based on the name of the navigation file (probably from the	)
  - What happens when there is a navigation file but no scientific file for this segment?
    - It is silently ignored.
  - What happens when there is a scientific file but no navigation file for this segment?
    - It is ignored printing an error message.
LoadTransectData:
Load data segment by segment and merge it in a single structure with a source list field, a tabular data field and sensor column fields.
Input may be a list of m-loaders or a directory of m-loaders.
ProcessGliderData:
Main processing function to generate filtered time series for each sensor.
Converts a tabular oriented structure to a structure of time series. This struct has the following fields (some of them may be missing):
  - navTime and sciTime
  - latitude and longitude
  - pitch
  - conductivity, temperature and pressure: ctd readings.
  - chlorophyll and turbidity: fluorescence and turibitdy sensor readings.
  - oxygen and oxygen_saturation: oxygen sensor readings.
  - DistanceOverGround: cumulated horizontal distance travelled.
  - salinity, density and depth: derived from ctd data.
  - continuousDepth: depth sequence without gaps.
  - profile_index: index identifying a valid profile ()
  - Tcor and Ccor: Sensor lag corrected temperature and conductivity sequences.
  - salinity_TH, salinity_Tcor_TH and salinity_Tcor_Ccor_TH: thermal lag corrected salinity using corresponding temperature and conductivity sequences.
  - timeseries: list of field names corresponding to a sequence of measurements.
  - correctionParams: thermal lag correction parameters applied.
  - waterInfo: water velocity information.
First do some preliminary regularization, selecting a time coordinate, interpolating spatial coordinates (latitude, longitude, and optionally pitch and depth) over selected time and optionally filtering badly referenced data. After that generate time series for the desired sensors and derived quantities. This is the detailed outline:
  - Select time coordinate and valid values:
    - m_present_time < sci_m_present_time < x
  - Select time-regular (no gaps) space position coordinates (latitude and longitude, and optionally depth and pitch):
    - m_gps_{lat,lon} < m_{lat,lon}
    - m_depth
    - m_pitch
      - Interpolate them over time if needed.
  - Discard data with no spatio-temporal reference.
    All records with missing time, lat or lon coordinates are discarded.
  - Select navigation time navTime previously selected time coordinate.
  - Select scientific time sciTime from available sensors.
    sci_m_present_time < sci_ctd41cp_timestamp < navTime
    - If scientific time filling option enabled, interpolate over navTime on missing values.
  - Select trajectory coordintes latitude and longitude as previously selected spatial coordinates.
  - Find transect time boundaries if commanded waypoints are present (otherwise all deployment is a big transect).
  - Select pitch if pitch sensor present otherwise set it to default value.
  - Select conductivity, temperature and pressure sensors (ctd).
    sci_water_{cond,temp,pressure} < m_water_{cond,temp,pressure}
    - In both cases convert pressure to decibars
  - Select chlorophyll and turbidity sensors.
    sci_flntu_{chlor,turb}_units
  - Select oxygen and oxygen_saturation sensors.
    sci_oxy3835_{oxygen,saturation}
  - Select water velocity and dead reckoning state information.
    m_final_water_{vx,vy} x_dr_state
  - Compute distanceOverGround (linear distance travelled by the glider in km) using selected latitude and longitude coordinates and m_lldist.
  - Filter pressure if available and option enabled.
  - Use seawater library to compute depth, salinity and density from ctd measurements (conductivity, temperature and pressure).
  - Check for desynchronized data if both times present and remove it if option enabled.
    - Bad records are the ones whose navigation and scientific time stamps differ more than a given theshold.
    - Actually the threshold is twice and a half the median navigation sampling period.
  - Compute continuousDepth interpolating depth (from ctd) over sciTime.
  - Compute profile_index identifying valid profiles. Look for start and end of profiles (upcasts and downcasts), check for profiles containing with a good ratio of valid depth (from ctd) readings and mark each record with the profile number or nan if profile is not good.
    - This is done to remove tails from previous profiles to be taken into account as proper profiles.
  - Compute temperature time constant if correction enabled in salinityCorrected option and temperature data available (from ctd).
    - Take it from tempTimeConstant option field if passed or compute it.
      - Median of time constant across consecutive profiles with opposite directions referenced to sciTime and depth.
    - If the time constant is not found it is removed from the correction option token list.
  - Compute conductivity time constant if correction enabled in salinityCorrected option and conductivity data available (from ctd).
    - Take it from condTimeConstant option field if passed or compute it.
      - Median of time constant across consecutive profiles with opposite directions referenced to sciTime and depth.
    - If the time constant is not found it is removed from the correction option token list.
  - Compute Tcor and Ccor correcting conductivity and temperature from sensor lag effects if corrections enabled in salinityCorrected option and time constants found.
  - Compute thermal lag parameters for combinations of {temperature, conductivity}, {Tcor, conductivity} and {Tcor, Ccor} using sciTime, depth and pitch if correction enabled in salinityCorrected option and conductivity data available (from ctd).
    - Take them from thermalParams and thermalParamsMeaning option fields if passed or compute them.
      - Median of thermal lag parameters across consecutive profiles with opposite directions referenced to sciTime and depth.
    - If the thermal lag parameters are not found, the correction is removed from the correction option token list.
  - Compute salinity_TH, salinity_Tcor_TH and salinity_Tcor_Ccor_TH correcting salinity from thermal lag effects using combinations of {temperature, conductivity}, {Tcor, conductivity} and {Tcor, Ccor} using sciTime, depth and pitch if correction enabled in salinityCorrected option and conductivity data available (from ctd).
    - Probably this does not work in the present version due to a possible bug in findGliderCorrectionParams: paramsMeaning struct should be build with string cell arrays with the name of the used variables ({'Tcor, Ccor'}) instead of option encoding arrays ('T_C_TH'). Probably this has not been observed because the porcessing option is TH only (no temperature or conductivity sensor lag correction).
  - Perform a range checking quality control for temperature and salinity.
    - Values out of range are set to nan.
  - Store list of computed time series as timeseries.
  - Store thermal lag parameters as correctionParams.
  - Store transect time boundaries as transects.
  - Store water velocity time series in its own struct as waterInfo.
GridGliderData:
Compute instantaneous regular vertical profiles of selected variables from profiles indetified in time series.
  - Non gridding variables are: latitude, longitude, distanceOverGround, navTime, sciTime, profile_index, depth, continousDepth and pressure.
    - So gridding variables are: pitch, temperature, conductivity, chlorophyll, turbidity, oxygen, oxygen_saturation, salinity, density, salinity_TH, salinity_Tcor_TH and salinity_Tcor_Ccor_TH.
  - Spatio-temporal coordinates of each profile are the mean coordinates over all samples in the profile.
  - Output is a struct with fields.
    - gridCoords: coordinate data struct with fields dephRange, latitudeRange, longitudeRange, timeRange, distanceRange. They are vectors with corresponding profile coordinates.
    - grids: struct with fields named after gridding variables. They are matrices containing column profiles.
    - meanProfiles: struct with fields named after gridding variables. They are scalars containing the corrsponding variable mean across all profiles.
    - stdProfiles: struct with fields named after gridding variables. They are scalars containing the corrsponding variable standard deviation across all profiles.
- GenerateScientificFigures:
## Dependencies
The toolbox depends on the following external tools:
1. Java PostgreSQL driver.
  It may be installed from the distribution repositories as a package libpg-java (renamed to libpostgresql-jdbc-java in Debian repositories at March 2012)-
  Add the corresponding jar file (/usr/share/java/postgresql.jar) to the dynamic java classpath with javaaddpath (javaaddpath('/usr/share/java/postgresql.jar')) or to the static path adding it to the list in classpath.txt (edit classpath.txt).
2. NetCDF library.
  Currently using snctools (MATLAB) or octcdf (Octave).
  For snctools follow instructions in the website.
  The octcdf package may be installed from the distribution repositories as a package octave-octcdf.
## Proposed configuration options
- database_access: struct with data base access parameters.
  - url
  - name
  - user
  - password
  - driver
- database_fields: struct mapping each deployment parameter field name with the corresponding column in the query.
  - name: deployment name.
  - glider: glider platform name.
  - start_date: deployment start date (seconds since POSIX epoch).
  - end_date: deployment end date (seconds since POSIX epoch).
- database_query: query to get the deployment parameters.
- local_paths: glider url patterns according to new filesystem layout.
  - binary
  - log
  - ascii
  - figures
  - netcdf_l0
  - netcdf_l1
  - netcdf_l2
- public_product_paths:
  - nc_l0
  - nc_l1
  - nc_l2
  - figure_description_json
  - figure_dir
## Proposed changes
- GetDeploymentsRemotely:
  - Switch to retrieve information from data base.
- GetDockserverFiles:
  - ?? Split structured arguments in basic arguments:
    - ftp url, user, and password.
    - Deployment/mission start date and time (default POSIX epoch) and end date and time (default now).
    - Target directory for binary and log files.
    - Glider name.
    - ?? remote binary and log paths.
- ConvertSlocumBinaries:
  - ?? Add option for path of conversion binaries.
  - Reimplement absolute path conversion function using fileattrib.
  - ?? Switch to conversion to dba, separated merge (newly implemented or using shipped executables), and dba2struct conversion function.
- Image output directory:
  - Switch ${outputDirs.imageBaseLocalPath}/${GLIDER}/${DEPLOYMENT} to 'figures' directory in glider deployment/mission data directory tree.
- LoadTransectData:
  - ListLoaders and SortLoaders:
    - ?? Change .ascii for folder at line 48.
    - Clean up unnecessary code in sortLoaders (use regex matches).
    - ?? Fusion ListLoaders and SortLoaders.
  - DealWithGlobalWorkspace
    - Simplify saving functionality.
  - Simplify ListLoaders.
  - Move sorting code to output function or use shipped sortrows.
- RemoveDuplicatedRecords:
  - Clarify option meaning.
  - Reimplement to allow different fill methods ('delete', 'first', 'last', 'mean').
- GenerateNcProduct, GetRawGliderVarAtts, GetProcGliderVarAtts and WriteGliderStaticMetadata:
  - Take out code for copying files to product public path (move it to main script).
  - ?? Add 'coordinates' attribute to variables.
  - Check for CF 1.6 conventions.
  - Check for attributes.
    - Latitude and longitude units: nmea, degrees.
  - Move code to function generating each level file.
  - Use external structs to pass variable attributes and global attributes as arguments.
- Nmea2deg;
  - Simplify code using fix and rem (deg = fix(nmea/100) + rem(nmea,100)/60)
- Introduce pre-processing/unit_conversion stage (previous to L0) to deal with:
  - Latitude and longitude nmea format.
- ProcessGliderData:
  - Add meta output argument to track processing issues:
    - interpolated variable values
  - Recode to avoid use of unnecessary variables (eval and clear constructs)
    - Note: probably was coded this way for some reason related to the fact that shipped m-loaders introduce global variables for each sensor.
  - Recode removing spatio-temporal unreferenced data section because there is an unnecessary double check.
  - Move desynchronized data removal code to a separate function.
  - Do desynchronized data removal in the regularization section prior to the computation of time series.
  - ?? Change identification of profile for a cleaner approach.
    - Create glider direction time serie marking the direction of the glider at each record with -1 for downcast, 1 for upcast and 0 for start/end points of upcasts and downcasts.
    - Change existing profile index time serie to all profiles numbered (decimal numbers at start/end of upcast/downcast).
    - Use function to validate a single profile.
  - Change sensor lag related code:
    - Do the parameter estimation and the correction in the same cell (loop over sensor) according to new option specification.
    - ?? Correct full serie instead of individual profiles.
  - Change thermal lag related code.
    - Do the parameter estimation and correction on the same cell (loop over sets of correction parameters).
    - ?? Correct full serie instead of individual profiles.
    - Adapt code for new option specification.
  - Move quality control code to its own function and call it from main script.
  - ?? Store water current information as any other timeserie.
  - ?? Index transects (traversal from one waypoint to an other) as did it for the profiles.
- FillScienceTime:
  - ?? Switch from interpolate over index (regular sampling assumption) to interpolate over navigation time.
    ASK MIGUEL: Are there scientific data records without scientific time?
    ASK MIGUEL: Are there navigation data records without navigation time?
- FindVariableTimeConstant:
  - ?? Move code to main processing function.
  - Split structured time serie input into time, depth, direction and variable sequences.
  - Add argument selecting the combining method ('mean', 'median', 'max', 'min') either as function handle or function name string (default to median).
  - Remove option argument and take debugPlot code out to main processing function.
- AdjustTimeConstant:
  - Split profile struct input arguments into time, depth and variable sequences.
  - Move nested function to sub-function.
- CorrectTimeResponse:
  - Simplify it using gradient or find already shipped function doing the same.
- FindGliderParams:
  - ?? Move code to main processing function.
  - Split structured time serie input into time, depth, direction, temperature and conductivity sequences.
  - Add argument selecting the combining method ('mean', 'median', 'max', 'min') either as function handle or function name string (default to median).
  - Remove option argument and take debugPlot code out to main processing function.
- AdjustThermalLagParams:
  - Split structured time serie input into time, depth, direction, temperature and conductivity sequences.
  - Move nested function to sub-function.
- CorrectThermalLag:
  - Split input profile structure into several arguments (time, depth, temperature, conductivity, pitch).
  - ?? Make pitch input mandatory or default it to 90º (perfectly vertical profile).
  - Make correction parameters argument mandatory.
    - Move default ones out to its own function.
  - Split output profile into temperature in cell and conductivity out of cell sequences.
- BuildPolygon:
  - Recode section computing area to avoid loop.
- GridGliderData:
  - Pass grid variable selection as argument.
- Main script
  - Split clearlier the stages: deployment listing, binary file downloading, binary file conversion, data processing and data output.
  - Use private product data paths configured in configuration section.
  - Convert only newly dowloaded files.
  - Remove unused variable missionId.
  - Use public products struct for public access to NetCDF and figures. It may contain the following fields:
    - NetCDF L0, L1 and L2 product public path (for THREDDS).
      If the field is present the corresponding product is copied to given path.
    - Figures public path url for images and json:
      If the field is present images are copied (linked?) to given path and a json file describing the figures is generated with the given name.
  - Copy/link output products at the end of whole processing chain if needed (based on output products struct).
  - Split sensor lag correction option into separated flags for each sensor. Each sensor has two option fields
    - enabling correction: true or false
    - correction parameters: struct with one field:
      - time constant (empty for estimation).
  - Change thermal lag correction option specification. There are two option fields:
    - enabling correction: true or false.
    - correction parameters: struct array with fields:
      - temperature serie to be used.
      - conductivity serie to be used.
      - constants ([a_o a_s t_o t_s], empty for estimation).
  - Call new function performing quality control.
  - Add grid variable options to configuration section.
    - variables to be gridded.
    - depth resolution.
  - Remove unused xmlImgsList variable.
## Open questions
1. Should file system layout and processing chain design be oriented towards a scheme based on
  1. glider > deployment
  2. glider > deployment > mission
2. Why ctd pressure is converted from bars to decibars?
  Probably because standard deriving functions from seawater toolbox (implementing UNESCO algorithms) want it this way.
3. Is it better to compute the corrected salinity inside the sensor cell or outside the sensor cell?
  Now is computed inside the cell.
  Is the pressure sensor inside or outside the sensor cell, or is it not directly related?
4. What is the output of oxygen concentration from the sci_oxy3835_oxygen sensor?
  Masterdata says nodim (ugh!).
  Aandera data sheet says uMol (micromolar, micromoles of oxygen per liter of solution).
  http://www.aadi.no/Aanderaa/Document%20Library/1/Data%20Sheets/Oxygen%20Optode%203835-4130-4175.pdf
5. Who is supposed to fill the geospatial deployment fields in the data base?
6. Location coordinates for each profile in gridded data product are obtained by a crude central estimate (mean or median). Would it be better to use interpolation over scattered data?
## File system layout
Future proposal:
- /home/glider
  - data_new or data_received or data_input: target folder for newly transmitted files for each glider (of current deployment).
    - ${GLIDER as platform_name-instrument_name}: logs and binaries downloaded from dockserver for current deployment of this glider.
  - data_nrt or data_rt: real time processed data for each glider and deployment.
    - ${GLIDER as platform_name-instrument_name}
      - ${DEPLOYMENT as deployment_date}
        - log
        - binary
        - ascii
        - netcdf
        - figures
  - data_dt: delayed time processed data.
    - ${GLIDER as platform_name-instrument_name}
      - ${DEPLOYMENT as deployment_date}
        - log
        - binary
        - ascii
        - netcdf
        - figures
  - deployments: target folder for glider deployment snapshots.
    - ${GLIDER as unit_name}
      - ${DEPLOYMENT as deployment_date}: snapshot files for this deployment of this glider.
      For slocum:
        - nav
        - sci
        - calibration
        - dockserver_01
        - dockserver_02
      For seaglider:
        - data
        - cfcard
        - calibration
        - basestation_01
        - basestation_02
## Deployment concept strucuture
For processing purposes a slocum glider deployment may be thought as having the following structure.
- deployment
  - mission 0
    - transect 0 (from waypoint 0 to waypoint 1)
      - mission segment 0
        - segment yo 0
          - downcast
          - upcast
        - segment yo 1
        - ...
      - mission segment 1
      - ...
    - transect 1 (from waypoint 1 to waypoint 2)
      - mission segment 2
      - …
    - ...
  - mission 1
    - transect 0
      - mission segment 0
      - mission segment 1
      - ...
    - transect 1
      - mission segment 2
      - …
    - …
  - ...